## Slide 1: Microgrids Overview
Josh Radoff (WSP)
Geoff Gunn (Arup)

## Slide 2
Why Microgrids Now?
Microgrids are a proxy for building and district scale projects that tackle resilience and carbon.
Generally part of infrastructure and building projects to support sustainability and resiliency goals.
New technologies have emerged and costs have come down: solar, batteries, controls
Emergence of innovative business models / P3 opportunities
 Microgrids are a means to an end!
 Everything we talk about has a strong business case.

## Slide 3
Utility Grid
Backup Generator
Building Load
Basic Building or Campus Electrical Configuration
Benefits:
Works!
Generally low cost

## Slide 4
Utility Grid
Backup Generator
Solar Array
Building Load
Add Solar
(or other onsite generation)
Common Elements
Net Meter with 2-way flow
Backup generation can be supplemented by solar
Benefits:
Reduced energy / cost
Third Party Finance
Reduced GHG

## Slide 5
Utility Grid
Generator (cogen, etc.)
Solar Array
Building Load
Microgrid
Add Island-ability = Microgrid
Common Elements
Critical load management (load controller)
Overall load and multiple generator control
Benefits:
Resiliency
Self Production
Decarbonization

## Slide 6
Utility Grid
Generator
Solar Array
Building Load
Microgrid
Storage
Electric Vehicles
Add Storage and More Controllable Loads
Common Elements
Storage can buffer peaks and support backup
EVs can be selectively charged based on grid conditions or solar availability
Benefits:
Batteries enable 24/7 use of solar, demand shaving, arbitrage
EVs represent easily curtailable load and eventually V2G
Enables Cost externalization

## Slide 7
Utility Grid
Solar Array
Building Load
Microgrid
Storage
Electric Vehicles
Over time: replace backup generator with more batteries
Benefits:
All electric
Zero carbon

## Slide 8
Architect:
Client:
Project:
Services:
Las Positas College Livermore, CA
Features:
District scale energy and microgrid system serving the entire campus
Includes solar array, microgrid, the district thermal energy, thermal and battery storage systems

## Slide 9
Architect:
Client:
Project:
Services:
Las Positas College Livermore, CA
Features:
District scale energy and microgrid system serving the entire campus
Includes solar array, microgrid, the district thermal energy, thermal and battery storage systems
National Western Center
Denver, CO

## Slide 10
Architect:
Client:
Project:
Services:
Monterey Bay Aquarium
Center for Ocean Education and
Leadership
Features:
Microgrid supplies power in the event of a grid outage
30kW rooftop solar PV system
200kWh battery system

## Slide 11
Battery Dispatch to Reduce Peak Demand
Resultant Load Before Batteries
Resultant Load After Batteries
Battery Discharging to Lower Peaks
Load Before Solar
4 MW Solar

## Slide 12
California Market Adjustment
Hour in Day | Jan. | Feb. | Mar. | Apr. | May | June | July | Aug. | Sept. | Oct. | Nov. | Dec.
1 | -$0.01 | -$0.01 | -$0.02 | -$0.02 | -$0.02 | -$0.01 | -$0.01 | $0.00 | -$0.01 | $0.00 | $0.00 | $0.00
2 | -$0.01 | -$0.02 | -$0.02 | -$0.02 | -$0.02 | -$0.02 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | $0.00 | $0.00
3 | -$0.01 | -$0.02 | -$0.02 | -$0.02 | -$0.02 | -$0.02 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | $0.00 | $0.00
4 | -$0.01 | -$0.02 | -$0.02 | -$0.02 | -$0.03 | -$0.02 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | $0.00 | $0.00
5 | -$0.01 | -$0.01 | -$0.02 | -$0.02 | -$0.02 | -$0.02 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | $0.00 | $0.00
6 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | $0.00 | -$0.01 | $0.00 | $0.00 | $0.00
7 | $0.00 | $0.01 | $0.00 | $0.00 | -$0.01 | -$0.02 | -$0.01 | $0.00 | $0.00 | $0.01 | $0.01 | $0.01
8 | $0.00 | $0.00 | $0.00 | -$0.01 | -$0.02 | -$0.02 | -$0.01 | $0.00 | -$0.01 | $0.01 | $0.02 | $0.02
9 | -$0.01 | -$0.01 | -$0.02 | -$0.02 | -$0.03 | -$0.02 | -$0.01 | -$0.01 | $0.00 | $0.00 | $0.01 | $0.01
10 | -$0.01 | -$0.02 | -$0.02 | -$0.02 | -$0.03 | -$0.02 | -$0.01 | -$0.01 | -$0.02 | -$0.01 | $0.00 | $0.00
11 | -$0.01 | -$0.02 | -$0.02 | -$0.03 | -$0.03 | -$0.02 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | $0.00
12 | -$0.01 | -$0.02 | -$0.03 | -$0.03 | -$0.03 | -$0.02 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | $0.00
13 | -$0.01 | -$0.03 | -$0.03 | -$0.03 | -$0.02 | -$0.02 | $0.00 | $0.00 | -$0.01 | -$0.01 | -$0.01 | -$0.01
14 | -$0.02 | -$0.02 | -$0.03 | -$0.03 | -$0.02 | -$0.01 | $0.00 | $0.00 | -$0.01 | -$0.01 | $0.00 | -$0.01
15 | -$0.01 | -$0.02 | -$0.03 | -$0.03 | -$0.02 | -$0.01 | $0.00 | $0.01 | $0.00 | -$0.01 | $0.00 | -$0.01
16 | -$0.01 | -$0.02 | -$0.03 | -$0.02 | -$0.02 | -$0.01 | $0.02 | $0.02 | $0.00 | $0.00 | $0.00 | $0.01
17 | $0.00 | -$0.01 | -$0.02 | -$0.02 | -$0.02 | $0.00 | $0.03 | $0.02 | $0.01 | $0.00 | $0.02 | $0.03
18 | $0.02 | $0.02 | -$0.01 | -$0.02 | -$0.01 | $0.00 | $0.04 | $0.04 | $0.02 | $0.05 | $0.05 | $0.02
19 | $0.01 | $0.01 | $0.00 | -$0.01 | $0.01 | $0.03 | $0.08 | $0.07 | $0.06 | $0.08 | $0.03 | $0.03
20 | $0.01 | $0.00 | $0.01 | $0.01 | $0.02 | $0.04 | $0.08 | $0.07 | $0.03 | $0.03 | $0.02 | $0.03
21 | $0.00 | $0.00 | $0.00 | $0.01 | $0.02 | $0.01 | $0.05 | $0.03 | $0.01 | $0.01 | $0.02 | $0.02
22 | $0.00 | $0.00 | $0.00 | $0.00 | $0.00 | $0.01 | $0.02 | $0.01 | $0.00 | $0.01 | $0.01 | $0.02
23 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | -$0.01 | $0.00 | $0.00 | $0.00 | $0.01 | $0.01 | $0.01
24 | -$0.01 | -$0.01 | -$0.02 | -$0.02 | -$0.02 | -$0.01 | $0.00 | $0.00 | -$0.01 | $0.00 | $0.00 | $0.01
2017 – 2018 average hourly Market Adjustment for each month:
largest credit:
spring around noon
largest charge:
summer and fall evenings

## Slide 13
Resultant Load After Batteries
Battery discharging to manage MPBA and demand charge
Day Ahead Market Price
Battery Dispatch to Optimize Market Rate Fluctuations

## Slide 14
District Energy (Thermal)
Benefits:
Enables cost externalization
Supports efficiency and electrification

## Slide 15
Amazon Campus Seattle, WA
Size: ~5 million square feet over 5 towers, meeting buildings, and spheres
Features:
District energy systems in urban environment
Heat recovery/reuse from nearby data center
Notes: General:
- Currently working on the 5th highrise building on the campus + "centers of energy" (low rise meeting buildings) + the spheres
- 1.1 MM each highrise building; Total ~5MM SF
Role:
- Mechanical/Plumbing, lighting design, design assist role
- Built ecology, full service on everything. Energy model, daylight model, spheres (comfort and light modeling)
District Energy
- Old converted parking garage to a data center, Amazon purchased the land from them.
- Brokering the deal was challenge
○ We were the technical arm in figuring out how this is going to work
○ Deal is predicated on how much heat is used
○ Tracking (M&V) to make sure amazon meets it’s obligations in terms of heat consumption
○ Amazon property development firm who led the charge, evangelist
○ We were the Amazon technical deal. They had their own engineer.
- Win - win for Amazon and data center owner
○ Data center saved on cooling tower use and water use
○ Allowed data center to expand
- 3rd party was created, owns the pipe across the street
- Harvests waste heat for the entire campus, use of hydronic heat in buildings
○ Enables all buildings to meet code with the same system
- Each building has it's own central plant
- Supplement with hot water boilers

## Slide 16
World Financial Center
New York, NY
Owner: Port Authority of NY & NJ
Features:
District scale chiller plant
Utilizes river water from the Hudson for cooling

## Slide 17
Transbay Transit Center San Francisco, CA
Size: 1.5 million sf
Features:
Geothermal system (uses more than 10 miles of high-density polyethelyne piping)
Supported by underground tidal flows
Short-term storage in the rain and graywater recovery tanks
Notes: Program Summary:
5.2M SF Office Space
1.06M SF Retail
2,000 Units Residential
700 Hotel Rooms
250,000 SF Food and Beverage
190,000 SF Entertainment

## Slide 18: Microgrid Optimization
Need to balance:
Resilience
Sustainability and
Costs
Traditional metrics to evaluate solution effectiveness are insufficient
Notes: Tweak bullet points to better speak to the various systems, and the challenges

## Slide 19: Microgrid Financing
Direct Capital
Lease
PPA/EaaS
Notes: Tweak bullet points to better speak to the various systems, and the challenges

## Slide 20: Microgrid Financing
Owner
Energy Service Provider
Project Risk
Operational Control
Direct Capital
Lease
PPA/EaaS
Notes: Tweak bullet points to better speak to the various systems, and the challenges

## Slide 21: Microgrid Financing
Availability of incentives
High electricity rates
Value of resilience of sustainability
Key factors to a bankable microgrid:
Notes: Tweak bullet points to better speak to the various systems, and the challenges

## Slide 22: Microgrid Financing
Availability of incentives
High electricity rates
Value of resilience of sustainability
Key factors to a bankable microgrid:
Need to identify the underlying business case early
Notes: Tweak bullet points to better speak to the various systems, and the challenges

## Slide 23
Notes: Tweak bullet points to better speak to the various systems, and the challenges

## Slide 24: Microgrid Adoption
Need to identify:
Local drivers and goals
Available levers
    Permitting
    DPU
    Codes
    Zoning
    etc.
Build consensus and stakeholder engagement
Notes: Tweak bullet points to better speak to the various systems, and the challenges

## Slide 25: Thank you !